## Slide 1: Here’s looking at you…
Geoff Huston

## Slide 2: The Theory
We use Google Ads to deliver a test script to a very large profile of users
  We measure the DNS, DNSSEC, IPv6, performance, and many other aspects of the end user’s view of the Internet
  We have some 500,000 ads delivered per day
  And each of them use uniquely generated URLs
  So, in theory we should see each unique URL retrieved once
  Right?

## Slide 3: Here is what we see in the web logs…
[22/Jan/2014:00:10:21 +0000]
  120.194.53.xxx
  "GET /1x1.png?t10000.u3697062917.s1390349413.i333.v1794.rd.td
[22/Jan/2014:00:11:29 +0000]
  221.176.4.xxx
  "GET /1x1.png?t10000.u3697062917.s1390349413.i333.v1794.rd.td
68 seconds later:
-- SAME URL
-- 120.194.53.xxx – Origin AS = 24445
-- 221.176.4.xxx – Origin AS = 9808

## Slide 4: How widespread is this?
48 days in 2013:
  29,171,864 unique URLS presented to end users
  612,089 of these URLS were re-presented to us from a different client IP address
That’s 2.1% of URLs fetches that seem to have attracted a digital stalker!

## Slide 5: The Top Repeaters
Rank IP Address Count AS AS Name
1 119.147.146.xxx 11,241 4134 CHINANET-BACKBONE No.31,Jin-rong Street CN
2 182.18.208.xxx 1,0982 23944 SKYBB-AS-AP AS-SKYBroadband SKYCable Corporation PH
3 182.18.209.xxx 5,046 23944 SKYBB-AS-AP AS-SKYBroadband SKYCable Corporation PH
4 124.6.181.xxx 5,046 4775 GLOBE-TELECOM-AS Globe Telecoms PH
5 112.198.64.xxx 4,641 4775 GLOBE-TELECOM-AS Globe Telecoms PH
6 203.177.74.xxx 3,315 4775 GLOBE-TELECOM-AS Globe Telecoms PH
7 120.28.64.xxx 3,230 4775 GLOBE-TELECOM-AS Globe Telecoms PH
8 211.125.138.xxx 3,098 9619 SSD Sony Global Solutions Inc. JP
9 210.94.41.xxx 1,414 6619 SAMSUNGSDS-AS-KR SamsungSDS Inc. KR
10 222.127.223.xxx 1,269 4775 GLOBE-TELECOM-AS Globe Telecoms PH
11 210.143.35.xxx 1,177 2516 KDDI KDDI CORPORATION JP
12 202.156.10.xxx 1,154 10091 SCV-AS-AP StarHub Cable Vision Ltd SG
13 14.1.193.xxx 1,128 45960 YTLCOMMS-AS-AP YTL COMMUNICATIONS SDN BHD MY
14 183.90.103.xxx 1,069 55430 STARHUBINTERNET-AS-NGNBN Starhub Internet Pte Ltd SG
15 202.246.252.xxx 995 2526 HITNET HITACHI,Ltd. Information Technology Division. JP
16 192.51.44.xxx 887 2510 INFOWEB FUJITSU LIMITED JP
17 183.90.41.xxx 774 55430 STARHUBINTERNET-AS-NGNBN Starhub Internet Pte Ltd SG
18 110.34.0.xxx 704 4007 Subisu Cablenet (Pvt) Ltd, Baluwatar, Kathmandu, Nepal NP
19 110.232.92.xxx 638 23679 NUSANET-AS-ID Media Antar Nusa PT. ID
20 37.19.108.xxx 603 44143 VIPMOBILE-AS Vip mobile d.o.o. RS
21 24.186.96.xxx 573 6128 CABLE-NET-1 - Cablevision Systems Corp. US
22 161.53.179.xxx 535 2108 CARNET-AS Croatian Academic and Research Network HR
23 193.254.230.xxx 534 25304 UNITBV Universitatea TRANSILVANIA Brasov RO
24 121.54.54.xxx 500 10139 SMARTBRO-PH-AP Smart Broadband, Inc. PH
77.244.114.xxx 484 42779 AZERFON Azerfon AS AZ

## Slide 6: Web Proxies?
A strong indicator of a proxy device is that it is located in the same AS as the end client.
So lets filter that list and look at those repeaters that use a different AS from the original request
And here’s what we see

## Slide 7: Different Origin AS Repeaters
Rank IP Address Count AS AS Name
1 119.147.146.xxx 8,886 4134 CHINANET-BACKBONE No.31,Jin-rong Street CN
2 220.181.158.xxx 493 23724 CHINANET-IDC-BJ IDC, China Telecommunications Corporation CN
3 123.125.161.xxx 446 4808 CHINA169-BJ CNCGROUP IP China169 Beijing Province Network CN
4 210.133.104.xxx 285 7677 DNP Dai Nippon Printing Co., Ltd JP
5 202.214.150.xxx 266 2497 IIJ Internet Initiative Japan Inc. JP
6 112.65.211.xxx 248 17621 CNCGROUP-SH China Unicom Shanghai network CN
7 221.176.4.xxx 226 9808 CMNET-GD Guangdong Mobile Communication Co.Ltd. CN
8 62.84.94.xxx 204 16130 FiberLink Networks LB
9 212.40.141.xxx 203 31126 SODETEL-AS SODETEL SAL LB
10 101.69.163.xxx 163 4837 CHINA169-BACKBONE CNCGROUP China169 Backbone CN
11 59.162.23.xxx 158 4755 TATACOMM-AS TATA Communications IN
12 8.35.201.xxx 156 15169 GOOGLE - Google Inc. US
13 118.186.36.xxx 149 23724 CHINANET-IDC-BJ IDC, China Telecommunications Corporation CN
14 190.96.112.xxx 147 262150 Empresa Provincial de Energia de Cordoba AR
15 202.155.113.xxx 143 4795 INDOSATM2-ID INDOSATM2 ASN ID
16 118.228.151.xxx 142 4538 ERX-CERNET-BKB China Education and Research Network Center CN
17 123.125.73.xxx 136 4808 CHINA169-BJ CNCGROUP IP China169 Beijing Province Network CN
18 69.41.14.xxx 133 47018 CE-BGPAC - Covenant Eyes, Inc. US
19 118.97.198.xxx 131 17974 TELKOMNET-AS2-AP PT Telekomunikasi Indonesia ID
20 112.215.11.xxx 128 17885 JKTXLNET-AS-AP PT Excelcomindo Pratama ID
21 122.2.0.xxx 125 9299 IPG-AS-AP Philippine Long Distance Telephone Company PH
22 176.28.78.xxx 123 197893 ELSUHD-AS Elsuhd Net Ltd. Communications and Computer Services IQ
23 14.139.97.xxx 120 55824 RSMANI-NKN-AS-AP National Knowledge Network IN
24 211.155.120.xxx 116 23724 CHINANET-IDC-BJ IDC, China Telecommunications Corporation CN
25 121.96.61.xxx 114 6648 BAYAN Bayan Telecommunications, Inc. PH

## Slide 8: Maybe its National Infrastructure
We’ve all heard about the Great Firewall of China
And other countries may be doing similar things
So perhaps these repeaters are the result of some form of national / regional content cache program
So lets filter this further by using geolocate information to find those cases where the original end client and the digital stalker locate to different countries

## Slide 9: Different Country Stalkers
Rank IP Address Count AS AS Name
1 119.147.146.xxx 7,001 4134 CHINANET-BACKBONE No.31,Jin-rong Street CN
2 8.35.201.xxx 156 15169 GOOGLE - Google Inc. US
3 190.216.130.xxx 84 3549 GBLX Global Crossing Ltd. AR
4 190.27.253.xxx 82 19429 ETB - Colombia CO
5 61.92.16.xxx 62 9269 HKBN-AS-AP Hong Kong Broadband Network Ltd. HK
6 208.80.194.xxx 53 13448 WEBSENSE Websense, Inc. US
7 112.140.187.xxx 33 45634 SPARKSTATION-SG-AP 10 Science Park Road SG
8 69.41.14.xxx 32 47018 CE-BGPAC - Covenant Eyes, Inc. US
9 126.117.225.xxx 31 17676 GIGAINFRA Softbank BB Corp. JP
10 113.43.175.xxx 29 17506 UCOM UCOM Corp. JP
11 202.249.25.xxx 26 4717 AI3 WIDE Project JP
12 139.193.204.xxx 25 23700 BM-AS-ID PT. Broadband Multimedia, Tbk ID
13 180.13.45.xxx 22 4713 OCN NTT Communications Corporation JP
14 201.221.124.xxx 21 27989 BANCOLOMBIA S.A CO
15 123.125.161.xxx 21 4808 CHINA169-BJ CNCGROUP China169 Beijing Province Network CN
16 220.181.158.xxx 17 23724 CHINANET-IDC-BJ IDC, China Telecommunications Corporation CN
17 208.184.77.xxx 17 6461 MFNX MFN - Metromedia Fiber Network US
18 183.179.254.xxx 16 9269 HKBN-AS-AP Hong Kong Broadband Network Ltd. HK
19 203.192.154.xxx 16 10026 PACNET Pacnet Global Ltd JP
20 139.193.223.xxx 13 23700 BM-AS-ID PT. Broadband Multimedia, Tbk ID
21 175.134.140.xxx 12 2516 KDDI KDDI CORPORATION JP
22 210.187.58.xxx 12 4788 TMNET-AS-AP TM Net, Internet Service Provider MY
23 195.93.102.xxx 12 1668 AOL-ATDN - AOL Transit Data Network GB
24 221.82.58.xxx 12 17676 GIGAINFRA Softbank BB Corp. JP
25 167.205.22.xxx 12 4796 BANDUNG-NET-AS-AP Institute of Technology Bandung ID

## Slide 10: Different Country Stalkers
Rank IP Address Count AS AS Name
1 119.147.146.xxx 7,001 4134 CHINANET-BACKBONE No.31,Jin-rong Street CN
2 8.35.201.xxx 156 15169 GOOGLE - Google Inc. US
3 190.216.130.xxx 84 3549 GBLX Global Crossing Ltd. AR
4 190.27.253.xxx 82 19429 ETB - Colombia CO
5 61.92.16.xxx 62 9269 HKBN-AS-AP Hong Kong Broadband Network Ltd. HK
6 208.80.194.xxx 53 13448 WEBSENSE Websense, Inc. US
7 112.140.187.xxx 33 45634 SPARKSTATION-SG-AP 10 Science Park Road SG
8 69.41.14.xxx 32 47018 CE-BGPAC - Covenant Eyes, Inc. US
9 126.117.225.xxx 31 17676 GIGAINFRA Softbank BB Corp. JP
10 113.43.175.xxx 29 17506 UCOM UCOM Corp. JP
11 202.249.25.xxx 26 4717 AI3 WIDE Project JP
12 139.193.204.xxx 25 23700 BM-AS-ID PT. Broadband Multimedia, Tbk ID
13 180.13.45.xxx 22 4713 OCN NTT Communications Corporation JP
14 201.221.124.xxx 21 27989 BANCOLOMBIA S.A CO
15 123.125.161.xxx 21 4808 CHINA169-BJ CNCGROUP China169 Beijing Province Network CN
16 220.181.158.xxx 17 23724 CHINANET-IDC-BJ IDC, China Telecommunications Corporation CN
17 208.184.77.xxx 17 6461 MFNX MFN - Metromedia Fiber Network US
18 183.179.254.xxx 16 9269 HKBN-AS-AP Hong Kong Broadband Network Ltd. HK
19 203.192.154.xxx 16 10026 PACNET Pacnet Global Ltd JP
20 139.193.223.xxx 13 23700 BM-AS-ID PT. Broadband Multimedia, Tbk ID
21 175.134.140.xxx 12 2516 KDDI KDDI CORPORATION JP
22 210.187.58.xxx 12 4788 TMNET-AS-AP TM Net, Internet Service Provider MY
23 195.93.102.xxx 12 1668 AOL-ATDN - AOL Transit Data Network GB
24 221.82.58.xxx 12 17676 GIGAINFRA Softbank BB Corp. JP
167.205.22.xxx 12 4796 BANDUNG-NET-AS-AP Institute of Technology Bandung ID

## Slide 11: Lets zoom in for a second
And look at the distribution of the clients who were stalked by 119.147.146.xxx
Which countries were the clients located?

## Slide 12
Rank Count Country
AE 27 United Arab Emirates
AG 2 Antigua and Barbuda
AL 32 Albania
AM 13 Armenia
AR 19 Argentina
AT 5 Austria
AU 21 Australia
AW 6 Aruba
AZ 8 Azerbaijan
BA 27 Bosnia and Herzegovina
BD 1 Bangladesh
BE 10 Belgium
BG 45 Bulgaria
BN 1 Brunei Darussalam
BO 1 Bolivia
BR 44 Brazil
BS 1 Bahamas
BY 7 Belarus
BZ 4 Belize
CA 125 Canada
CL 13 Chile
CN 4,622 China
CO 11 Colombia
CR 1 Costa Rica
CW 2 Curaçao
CY 1 Cyprus
CZ 37 Czech Republic
DE 21 Germany
DO 2 Dominican Republic
DZ 19 Algeria
EC 8 Ecuador
EG 22 Egypt
ES 38 Spain
FR 68 France
GB 45 United Kingdom
GE 12 Georgia
GR 25 Greece
GY 1 Guyana
HK 721 Hong Kong
HN 1 Honduras
HR 9 Croatia
HU 67 Hungary
ID 159 Indonesia
IE 16 Ireland
IL 8 Israel
IN 32 India
IQ 21 Iraq
IT 52 Italy
JM 5 Jamaica
JO 2 Jordan
JP 2,910 Japan
KE 1 Kenya
KG 1 Kyrgyzstan
KH 28 Cambodia
KR 27 Republic of Korea
KW 1 Kuwait
KZ 11 Kazakhstan
LA 6 Laos
LK 11 Sri Lanka
LT 12 Lithuania
LV 6 Latvia
MA 6 Morocco
MD 2 Republic of Moldova
ME 7 Montenegro
MK 69 Macedonia
MM 2 Myanmar
MN 36 Mongolia
MO 37 Macao
MP 4 Northern Mariana Islands
MT 4 Malta
MU 7 Mauritius
MX 107 Mexico
MY 375 Malaysia
NC 1 New Caledonia
NI 1 Nicaragua
NL 15 Netherlands
NO 8 Norway
NP 1 Nepal
NZ 20 New Zealand
OM 1 Oman
PA 11 Panama
PE 29 Peru
PH 166 Philippines
PK 1 Pakistan
PL 340 Poland
PR 7 Puerto Rico
PS 9 Occupied Palestinian Territory
PT 1 Portugal
RO 197 Romania
RS 62 Serbia
RU 32 Russian Federation
RW 1 Rwanda
SA 24 Saudi Arabia
SE 3 Sweden
SG 83 Singapore
SI 13 Slovenia
SK 13 Slovakia
SR 2 Suriname

## Slide 13
SV 3 El Salvador
TH 138 Thailand
TN 3 Tunisia
TR 57 Turkey
TW 1,241 Taiwan
UA 37 Ukraine
US 371 United States of America
UZ 1 Uzbekistan
VC 1 Saint Vincent and the Grenadines
VE 16 Venezuela
VN 249 Vietnam
YE 1 Yemen

## Slide 14: What the…?
That’s an impressive list of countries!
And our collection of 30 million URLs across 49 days is a mere drop in the ocean of web fetches on the Internet
So are we glimpsing here the tip of some much larger program of URL stalking?

## Slide 15: Accident? Deliberate? Something Else?
Why go to all the trouble to collect URLs but use the same IP address to perform the followup stalking?
Is this some kind of deliberate leakage from a middleware device?
Or the result of some kind of a virus?
Or the outcome of TOR + virus?
Or a smart, but at the same time remarkably dumb, digital stalking program?
Or <insert your favourite conspiracy theory here>