## Slide 1: DNS, DNSSEC and DDOS
Geoff Huston
APNIC
February 2014

## Slide 2: The Evolution of Evil
It used to be that they sent evil packets to their chosen victim
  but this exposed the attacker, and limited the damage they could cause
Attacker
Victim
e.g. TCP SYN attack

## Slide 3: The Evolution of Evil
Then they enrolled a bot army to send evil
  which kept the attacker hidden and increased the damage leverage
Attacker
Victim
Massed URL retrieval
Experiences what
looks like a
TCP syn attack!

## Slide 4: The Evolution of Evil
But now they co-opt the innocent to the evil cause, and use un-corrupted servers to launch the attack
  which hides the attacker(s) and uses the normal operation of servers to cause damage

## Slide 5: UDP is a Fine Protocol
UDP is used whenever you want a fast and highly efficient short transaction protocol
Send a query to a server ( one packet)
And the server sends an answer (one packet)
UDP works best when the question and the answer are small (<512 bytes), but can work on larger transactions *
Although it’s not as reliable as TCP
The fine print – you‘ll need to magnify this to read it!
Some UDP applications use multiple UDP packets for large answers (e.g. NTP). Some rely of IP level fragmentation (e.g. DNS with EDNS0)
The problem with relying on fragmentation is firewall filtering and NATs (the trailing frags have no transport level header to assist in locating the NAT binding , as fragmentation is an IP level function)
And the problem with multiple UDP packets is reliably reassembly is pushed into the application, which may not necessarily do this well!
*

## Slide 6: UDP Mutation
Unlike TCP there is no handshake between the two parties who are communicating
  Send the server a UDP packet
  The server flips the source and destination IP addresses and responds with a UDP packet
  The server never checks the authenticity of the source address
This allows a simply reflection attack…

## Slide 7: UDP Reflection Attack
Attacker
Victim
Server
Proto: UDP
Dest: Server
Source: Victim
Proto: UDP
Dest: Victim
Source: Server
Note the fake source!

## Slide 8: UDP and DDOS Reflection Attacks
This works “best” for a UDP-based service when
  The service is widely used
  Servers are commonplace
  Servers are poorly maintained (or unmaintained)
  Clients are not “qualified” by the server (i.e. anyone can pose a query to a server)
  The answer is far bigger than the question

## Slide 9: Hmmmmm
What could that be?

## Slide 10: DNS as an attack vector
  UDP-based query response service
    UDP is now almost ubiquitous for the DNS – EDNS0 wiped out the last vestiges of TCP fallback
  The service is widely used
    Everybody is a client of the DNS
  Servers are commonplace
    Resolvers are scattered all over the Internet
  Servers are poorly maintained (or unmaintained)
    There are some 30 million open resolvers
  Clients are not “qualified” by the server (i.e. anyone can pose a query to a server)
    DNS servers are by design promiscuous
    Many DNS resolvers are unintentionally promiscuous
  The answer is far bigger than the question
    Just ask the right DNS question!

## Slide 11: DNS and DDOS
DNS DDOS attacks are now very commonplace on today’s Internet
They can (and do) operate at sustained gigabit speeds
They can use corrupted intermediaries to broaden the attack surface and further increase the query intensity
And efforts to mitigate at the server tend to degrade the quality of the DNS service, as well as affecting the victim

## Slide 12: DNS Queries and Responses
dig A isc.org - query size = 36 bytes
149.20.64.69 – response size = 52 bytes
Conventional DNS queries and answers tend to be relatively poor attack amplifiers – in general the answer is not all that much larger than the question
But there are particular questions that generate more impressive answers…

## Slide 13: The DNS ANY query
dig ANY isc.org – query size = 36 bytes
response size = 3,587 bytes
That’s more like it! In this case the response is 100x larger than the query

## Slide 14: Blocking the ANY attack
Modify the resolver not to respond to ANY queries in a meaningful way
$ dig ANY isc.org @8.8.8.8
; <<>> DiG 9.8.3-P1 <<>> ANY isc.org @8.8.8.8
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: SERVFAIL, id: 6696
;; flags: qr rd ra; QUERY: 1, ANSWER: 0, AUTHORITY: 0, ADDITIONAL: 0
;; QUESTION SECTION:
;isc.org. IN ANY
;; Query time: 632 msec
;; SERVER: 8.8.8.8#53(8.8.8.8)
;; WHEN: Sun Feb 16 09:42:48 2014
;; MSG SIZE rcvd: 25

## Slide 15: The DNSSEC query
With DNSSEC, if the client requests DNSSEC information, then the additional records in the response contain crypto values
These crypto records can be quite large…
dig +dnssec A isc.org – query = 36 bytes
149.20.64.69 – response = 1,619 bytes
That’s an additional 1,567 bytes of crypto payload that has been provided by DNSSEC

## Slide 16: Blocking DNSSEC DNS attacks
Stop serving DNSSEC-signed zones
And/or configure resolvers to turn off the DNSSEC-OK EDNS0 flag
But resolver-level query blocking defeats the entire purpose of DNSSEC!
So we need to look to other measures to mitigate this vulnerability

## Slide 17: Possible responses
Drop “excessive” queries at the resolver
  collateral damage to the server and the served names
  can lead to cache poisoning attacks
Drop EDNS0 and revert to original DNS behaviour
  No DNS UDP responses over 512 bytes
  Requestor directed to use TCP instead
  Poor DNS resolution performance for all clients
  Can lead to server overload though increased TCP load
Maybe we can combine the two approaches

## Slide 18: DNS Response Rate Limiting (RRL)
Set a maximum rate that any requestor will be told the same answer
    note: this is not about the query – its about the response!
Above this threshold either drop the query, or respond with the query and the truncated bit (TC) set ON
  The ratio of candidate queries to TC responses is termed the “SLIP ratio”
    Some folk say SLIP=2 is enough
    Others seem to prefer SLIP=1

## Slide 19: This will not eliminate the problem
As the attacker can broaden the attack plane across a large set of open recursive resolvers and not overload any single resolver to trigger its local RRL response
  And there are some ~30M such open resolvers
  http://openresolverproject.org
But it does increase the effort required to mount an attack based on DNS reflection, due to the added need to distribute the attack profile over a large set of resolvers
Attackers tend to exert no more effort than is strictly necessary to achieve the desired outcome, so increasing the effort needed to use the DNS to mount a reflection attack may well shift attention to other vulnerabilities, such as NTP

## Slide 20: What you need to be naughty
Generate a list of open resolvers (zmap, for example is a good starting point)
Write a simple script that sends a simple DNS query to an open resolver, with UDP source address spoofing
Enlist a collection of coercible hosts to generate some 250,000 DNS queries per second across your list of open resolvers
And the servers will respond with a 300Mbps DDOS stream!
Rinse, repeat and multiply
To Do List

## Slide 21: What you need to be nice
Add RRL to your DNS resolvers
Clean up open DNS resolvers in your networks
  Limit queries on recursive resolvers to be sourced from your client cone, if you can

## Slide 22: But…
Being nice is not always possible
  There is a significant volume of embedded DNS functionality in appliances and NAT-based consumerware
  And enough of includes open DNS resolver functionality to be a problem that is not going to be “fixed” anytime soon

## Slide 23: It’s not just the DNS
NTP uses a UDP-based command and control channel over the same port as the time exchange (UDP port 123)
And NTP servers are often installed with an open config
The NTP monlist command is 220 bytes to send, and the response is a set of packets with a total volume of 46,800 bytes

## Slide 24: What you need to be nice
Add RRL to your DNS resolvers
Clean up open DNS resolvers in your networks
  Limit queries on recursive resolvers to come from your client cone, if you can
While you are at it, do the same filtering for NTP, and the monlist command in particular

## Slide 25: In the longer term…
Commonly used protocols that can generate large UDP responses are a long term problem
  And DNSSEC will not cram into a 512 byte payload in the DNS
So maybe it’s the ability to pass through IP packets through the network with a false IP source address that is the basic problem, and just UDP exposes this problem to application level behaviour

## Slide 26: What you need to be nice
Add RRL to your DNS resolvers
Clean up open DNS resolvers in your networks
  Limit queries on recursive resolvers to come from your client cone, if you can
While you are at it do the same filtering for NTP, and the monlist command in particular
Perform outbound traffic filtering to support source address validation: BCP38

## Slide 27: Some Useful Resources
Open DNS resolvers:
  http://openresolverproject.org
DNS RRL description
  http://www.redbarn.org/dns/ratelimits
Sealing up NTP – a template for ntp.conf
  http://www.team-cymru.org/ReadingRoom/Templates/secure-ntp-template.html
Open NTP servers
  http://openntpproject.org
BCP 38
  http://bcp38.info
BCP 38 tracking
  http://spoofer.cmand.org//

## Slide 28
Thanks!