## Slide 1: An Update on Mobility in Today’s Internet
Geoff Huston,
APNIC Labs

## Slide 2: Counting Platforms
http://statcounter.com/
8.5%
4.3%
Mobiles are now
40% of all visible devices

## Slide 3: Counting the Money
http://statcounter.com/
8.5%
4.3%
Mobiles are now
40% of all visible devices
Mobile access services represent
75% of all Access Provider revenue

## Slide 4: Mobile Production Numbers
  2014: 1.5 billion units shipped
  Factors:
    Production volumes are bringing down component unit cost
    Android is bringing down software unit cost
    No need for new content - leverage off the the existing web universe of content
    Shift away from the desktop and the laptop by the production industry seeking new markets for their production capability

## Slide 5: Who’s playing
Android
  84% of all smartphone shipments in 2014
  Multi-vendor adoption
  Android also extending into tablets and large screens
Apple iPhone / iPad
  12% of all smartphone shipments in 2014
  Revenues for Apple: $182B in 2014
Windows
  3% market share
  Mostly Lumia models with Nokia

## Slide 6: We used to think…
That the mobile market was the market “driver” for the Internet
  Mobiles represent the highest revenue sector, and show the highest growth numbers
  And this is still true today
That the true driver for IPv6 adoption in the Internet was in the mobile sector
  If mobile platforms went to IPv6 then everyone else would be forced to follow
  But maybe this is not so true today.

## Slide 7: One Mobile Technology?
GSM revolutionised the mobile industry by offering a single technology standard and a single business model across a large part of the mobile market
Roaming just worked in the GSM world
Has the mobile industry managed to stay in lock step as it moves into the 4G world?

## Slide 8: One Mobile Technology? Not!
The mobile industry is now very heterogeneous
  Various spectrum allocations and regulatory constraints
  Various service objectives
  Various operator business objectives (incumbent vs challenger)
  Radically different objectives from handset suppliers vs network carriage operators
  3G is the LCD for roaming – 4G is more random!

## Slide 9: The Mobile IPv6 Story
The result is that the approach to IPv6 transition is highly fragmented across the operators and across handsets
The result is the deployment of various permutations of transitional IPv4 and IPv6 support in the mobile environment:
  Native mode dual stack over LTE: e.g. Verizon
  IPv4 layered over native IPv6, 464 XLAT: e.g. T-Mobile
  IPv4 synthesized over native IPv6 with NAT64 support
  IPv6 tunnelled over IPv4

## Slide 10: The Mobile IPv6 Story
The result is that the approach to IPv6 transition is highly fragmented across the operators and across handsets
The result is the deployment of various permutations of transitional IPv4 and IPv6 support in the mobile environment:
  Native mode dual stack over LTE: e.g. Verizon
  IPv4 layered over native IPv6, 464 XLAT: e.g. T-Mobile
  IPv4 synthesized over native IPv6 with NAT64 support
  IPv6 tunnelled over IPv4
This diversity implies that many operators have unique requirements for network and device capabilities
Which implies the imposition of cost and complexity for the service operators through customization of technologies
Which all adds to the cost of service to consumers
Nobody wins from this fragmented transition scenario!

## Slide 11: Dual Stack vs Mono Stack
IPv6 only access network
  Single NAT64 at the network edge to map external IPv4 services to local IPv6 addresses
  or
  4-to-6 mapping in the handset and 6-to-4 mapping at the network edge to provide a NAT+XLATE based IPv4 service
Dual Stack access
  Pass IPv6 and IPv4 all the way through to the handset

## Slide 12: Mobile Devices and IPv6
iOS
  No OS preference for IPv6 – uses a mechanism that should result in an approximate 50/50 split between IPv6 and IPv4 for dual stack
  Browsers may add their own IPv6 selection bias
  We saw in August 2015 1,216,594 iOS devices
    64,740 responded in IPv6 (5%)
    46,784 preferred to use IPv6 (72%)
  iOS 9 beta changes this behaviour to prefer IPv6 in dual stack contexts
  No currently planned support for 464XLAT – proposes a NAT64 solution to single protocol access networks

## Slide 13: Mobile Devices and IPv6
Android
  No preference for IPv6 – uses a mechanism that should result in an approximate 50/50 split between IPv6 and IPv4 for dual stack
  Browsers may add their own IPv6 selection bias
  We saw in August 2015 3,353,463 iOS devices
    175,922 responded in IPv6 (5%)
    151,754 preferred to use IPv6 (86%)
  No current plans to add any bias to use IPv6
  Has support for 464XLAT
  Does not support DHCPv6 (prefers RA and PD framework)

## Slide 14: It’s not just Transitional Complexities
It’s also the issue of Wifi Handoff and/or multi-path support
  The traditional mobile providers operate with exclusive access to spectrum within defined locales (with associated license costs)
  Alternate access competitors can operate in unlicensed spectrum with WiFi network services
  Handsets are also entering the space with platform services that support connection agility across diverse access networks
  Mobile incumbents are being forced to chase this alternate access market or risk losing market share
  And here there are visible cracks in the protocol stack!

## Slide 15: The Mobile Stack Model
Access Network Services
OS Platform Library
Application

## Slide 16: Cracks in the Stack
Access Network Services
Access Network Services
Access Network Services
Virtual Connection Server
Virtual Connection Client
OS Platform Library
Application
Access Network Services
The Google Fi Approach:
OS-Controlled Seamless
Handoff Agility

## Slide 17: Cracks in the Stack
Access Network Services
Access Network Services
Access Network Services
MP-TCP Server
MP-TCP
OS Platform Library
Application
Access Network Services
The MP-TCP Approach:
Apple’s Siri
Application-Controlled
Handoff Agility
Internet

## Slide 18: Cracks in the Stack
Access Network Services
Access Network Services
Access Network Services
Raw IP
OS Platform Library
Application
Access Network Services
The Application Approach: Facebook
Fold the entire transport
session control into the
application
Application Library

## Slide 19: Cracks in the Stack
Access Network Services
Access Network Services
Access Network Services
Raw IP
Application
Access Network Services
The VPN Application Approach:
Hide the application traffic from both the local platform as well as the local network
Application Library
Virtual Connection Server
Virtual Connection Client

## Slide 20: Where now for Mobiles?
Mobile Carriage Operators are being pushed into undistinguished utility roles
  No more voice premiums
  Erosive pressure on data service margins
  OS and App providers splitting away from carrier constraints
Mobile Device manufacturers are being squeezed (except Apple)
Google and Apple now control the platform space
So apps are now turning on their over versions of paranoia!

## Slide 21: Where now for Mobiles?
Consumers want more for less
  The rise of the Streamers
  (much) higher download speeds
  (much) larger data caps
  Lower premiums
  Competitive pressure on providers to response to this consumer pressure

## Slide 22: Where now for Mobiles?
Exclusive Use radio spectrum is too expensive
  Are they pricing themselves out of the consumer market?
  WiFi access and application handover approaches are placing pressure on the traditional mobile operator’s margins
  If the cellular providers want cheaper carriage then they need to look at augmenting their offering with WiFi base station handoff infrastructure

## Slide 23: Where now for Mobiles?
The underlying observation here is that the mobile network operator has lost control of the mobile access device and the services offerred across the mobile network
  And after losing that control there is no way back!
  The device vendor and its applications are charting a course that is in direct conflict with the mobile network operator’s desires, and managing to monetize this far more efficiently than the mobile network operator
  Which means that there is increasing pressure to increased shared unregulated spectrum and increasing discontent with the behaviour of the exclusive spectrum holders
  Mobile operators are trying to seize the initiative with WiFi handoff, while OS platforms and Apps are trying to place themselves in control and constrain the mobile providers into limited cellular data role

## Slide 24: Thank You!
Questions?