## Slide 1: An Update on Mobility in Today’s Internet
Geoff Huston,
APNIC Labs
November 2015

## Slide 2: Why?
Why should we be concerned about the mobile Internet environment?

## Slide 3: Why?
Why should we be concerned about the mobile Internet environment?
Because everybody else is!

## Slide 4: Counting Platforms
http://statcounter.com/
8.5%
4.3%

## Slide 5: Counting Platforms
http://statcounter.com/
8.5%
4.3%
Mobiles are now
40% of all visible devices

## Slide 6: Counting the Money
http://statcounter.com/
8.5%
4.3%
Mobiles are now
40% of all visible devices
Mobile access services represent
75% of all Access Provider revenue

## Slide 7: Mobile Production Numbers
  2014: 1.5 billion units shipped
  Factors:
    Production volumes are bringing down component unit cost
    (unit fabrication cost is close to USD 50)
    Android is bringing down software unit cost
    No need for new content - leverage off the the existing web universe of content
    Shift away from the desktop and the laptop by the chip production industry seeking new markets for their production capability

## Slide 9: Who’s playing
Android
  84% of all smartphone shipments in 2014
  Multi-vendor adoption
  Android also extending into tablets and large screens
Apple iPhone / iPad
  12% of all smartphone shipments in 2014
  Revenues for Apple: $182B in 2014
Windows
  3% market share
  Mostly Lumia models with Nokia

## Slide 10: Device Market Share

## Slide 11: One Mobile Technology?
GSM revolutionised the mobile industry by offering a single technology standard and a single business model across a large part of the mobile market
Roaming just worked in the GSM world
Has the mobile industry managed to stay in lock step as it moves into the 4G world?

## Slide 12: One Mobile Technology?
GSM revolutionised the mobile industry by offering a single technology standard and a single business model across a large part of the mobile market
Roaming just worked in the GSM world
Has the mobile industry managed to stay in lock step as it moves into the 4G world?
Ha! In your dreams!

## Slide 13: One Mobile Technology - Not!
The mobile industry is now very heterogeneous
  Various spectrum allocations and regulatory constraints
  Various service objectives
  Various operator business objectives (incumbent vs challenger)
  Radically different objectives from handset suppliers vs network carriage operators
  4G services largely share only the name “4G” – the rest is more random!

## Slide 14: Who’s in control? Mobiles!
The mobile market is the market “driver” for Internet technology:
  The PC and laptop market is in terminal decline
  Mobiles represent the highest revenue sector, and show the highest growth numbers
  The mobile Market was born and raised on NATs
    The IPv4 model for cellular mobile service is still heavily based on CGNs and a liberal dose of application level proxies and gateways

## Slide 15: Implications for IPv6
The true driver for IPv6 adoption in the Internet is in the mobile sector
  If mobile platforms went to IPv6 then everyone else would be forced to follow!
  So what can we say about IPv6 and mobiles?

## Slide 16: The Mobile IPv6 Story
The approach to IPv6 transition is highly fragmented across the operators and across handsets
  IPv4 access network
    tunnel IPv6 in a conventional (or unconventional) 6-in-4 encapsulation
  IPv6 access network
    Used in 464 XLAT:
      Translate V4 into V6 across the access network and reverse translate in the device to present IPv4 interface to applications
    Advocated by Apple:
      Translate V4 into V6 across the access network (with support of DNS64) and present IPv6 interface to applications
  Dual Stack access network

## Slide 17: The Mobile IPv6 Story
The approach to IPv6 transition is highly fragmented across the operators and across handsets
  IPv4 access network
  tunnel IPv6 in a conventional 6-in-4 encapsulation
  IPv6 access network
    Used in 464 XLAT:
      Translate V4 into V6 across the access network and reverse translate in the device to present IPv4 interface to applications
    Advocated by Apple:
      Translate V4 into V6 across the access network (with support of DNS64) and present IPv6 interface to applications
  Dual Stack access network
This diversity implies that many operators have unique requirements for network and device capabilities

## Slide 18: The Mobile IPv6 Story
The approach to IPv6 transition is highly fragmented across the operators and across handsets
  IPv4 access network (3GPP model)
  tunnel IPv6 in a conventional 6-in-4 encapsulation
  IPv6 access network
    Used in 464 XLAT:
      Translate V4 into V6 across the access network and reverse translate in the device to present IPv4 interface to applications
    Advocated by Apple:
      Translate V4 into V6 across the access network (with support of DNS64) and present IPv6 interface to applications
  Dual Stack access network
This diversity implies that many operators have unique requirements for network and device capabilities
Which implies the imposition of cost and complexity for the service operators through customization of technologies

## Slide 19: The Mobile IPv6 Story
The approach to IPv6 transition is highly fragmented across the operators and across handsets
  IPv4 access network (3GPP model)
  tunnel IPv6 in a conventional 6-in-4 encapsulation
  IPv6 access network
    Used in 464 XLAT:
      Translate V4 into V6 across the access network and reverse translate in the device to present IPv4 interface to applications
    Advocated by Apple:
      Translate V4 into V6 across the access network (with support of DNS64) and present IPv6 interface to applications
  Dual Stack access network
This diversity implies that many operators have unique requirements for network and device capabilities
Which implies the imposition of cost and complexity for the service operators through customization of technologies
Which all adds to the cost of service to consumers

## Slide 20: The Mobile IPv6 Story
The approach to IPv6 transition is highly fragmented across the operators and across handsets
  IPv4 access network
  tunnel IPv6 in a conventional 6-in-4 encapsulation
  IPv6 access network
    Used in 464 XLAT:
      Translate V4 into V6 across the access network and reverse translate in the device to present IPv4 interface to applications
    Advocated by Apple:
      Translate V4 into V6 across the access network (with support of DNS64) and present IPv6 interface to applications
  Dual Stack access network
This diversity implies that many operators have unique requirements for network and device capabilities
Which implies the imposition of cost and complexity for the service operators through customization of technologies
Which all adds to the cost of service to consumers
Nobody wins from this fragmented transition scenario!

## Slide 21: Mobile Devices and IPv6
iOS
  Until iOS 9 there was no OS preference for IPv6
    iOS used a mechanism that was meant to result in an approximate 50/50 split between IPv6 and IPv4 for dual stack
  Browsers and other apps may add their own IPv6 selection bias on top of the OS library

## Slide 22: Mobile Devices and IPv6
iOS
  Measurement:
  We saw in August 2015 1,216,594 iOS devices accessing Dual Stack services
    64,740 responded in IPv6 (5% of seen iOS devices)
    46,784 preferred to use IPv6

## Slide 23: Mobile Devices and IPv6
iOS
  iOS 9 changed this behaviour to prefer IPv6 in dual stack contexts
    iOS 9 is reported to use a 25ms bias timer
  No currently planned support for 464XLAT in the device
    Apple proposes a NAT64 solution to single protocol access networks
    Applications are “encouraged” to ensure that they can operate in a IPv6 environment, potentially assisted by a back end NAT64 gateway

## Slide 24: Mobile Devices and IPv6
Android
  No preference for IPv6 – uses a mechanism that should result in an approximate 50/50 split between IPv6 and IPv4 for dual stack
    No public commitment to change this behaviour
  Browsers and other apps may add their own IPv6 selection bias

## Slide 25: Mobile Devices and IPv6
Android
  Measurement
  We saw in August 2015 3,353,463 Android devices
    175,922 responded in IPv6 (5% of seen android devices)
    151,754 preferred to use IPv6

## Slide 26: Mobile Devices and IPv6
Android
  No current plans to add any bias to use IPv6
  Has support for 464XLAT
  Does not support DHCPv6 (prefers RA and PD framework)

## Slide 27: It’s not just Transitional Complexities…
Mobiles are multi-interface devices:
  Cellular radio
    High unit cost, variable quality and speed, broad coverage
  WiFi
    Low cost, better quality and speed, tethered-style coverage
  Bluetooth
    Low cost, very limited radius
  USB (Ethernet)
    Low cost, high quality and speed, physically tethered

## Slide 28: It’s not just Transitional Complexities…
Mobiles are multi-interface devices:
  Cellular radio
    High unit cost, variable quality and speed, broad coverage
  WiFi
    Low cost, better quality and speed, tethered-style coverage
  Bluetooth
    Low cost, very limited radius
  USB (Ethernet)
    Low cost, high quality and speed, physically tethered
Can we take advantage of these multiple interfaces to improve speed and quality and also control costs?

## Slide 29: It’s not just Transitional Complexities…
Which leads multi-interface support and the matter of “Live Handoff”

## Slide 30: Live Handoff
Can an live application switch between cellular radio and wireless services without dropping the call?

## Slide 31: Live Handoff
Can an live application switch between cellular radio and wireless services without dropping the call?
Why is this an important question?

## Slide 32: Live Handoff
The traditional mobile providers operate with exclusive access to spectrum within defined locales (with associated license costs)
Alternate access competitors can operate almost anywhere in unlicensed spectrum with WiFi network services
Devices now include platform services that support connection agility across diverse access networks
Customers see higher utility and (hopefully) lower costs for mobility services
Cellular access operators see revenue erosion issues

## Slide 33: Live Handoff
The traditional mobile providers operate with exclusive access to spectrum within defined locales (with associated license costs)
Alternate access competitors can operate almost anywhere in unlicensed spectrum with WiFi network services
Devices now include platform services that support connection agility across diverse access networks
Customers see higher utility and (hopefully) lower costs for mobility services
Cellular access operators see revenue erosion issues
The billion dollar question is: Who gets to control this handoff between licensed and unregulated radio access services?

## Slide 34: The “basic” Mobile Stack Model
Access Network Services
OS Platform Library
Application
WiFi
Cellular
Bluetooth
USB

## Slide 35: The VPN approach
WiFi
Cellular
USB
Access Network Services
Raw IP
Application
Access Network Services
The VPN Application Approach:
Hide the application traffic from both the local platform as well as the local network
Application Library
Virtual Connection Server
Virtual Connection Client

## Slide 36: The Application View
Access Network Services
Raw IP
OS Platform Library
FBApplication
Access Network Services
The Application Approach: Facebook
Fold the entire transport
session control into the
application
FBApplication Library
WiFi
Cellular
Bluetooth
USB
Facebook DC

## Slide 37: MP-TCP controller - Siri
Access Network Services
MP-TCP Server
MP-TCP
OS Platform Library
Application
Access Network Services
The MP-TCP Approach:
Apple’s Siri
Application-Controlled
Handoff Agility
Internet
WiFi
Cellular
USB

## Slide 38: The cellular access operator’s preferred response
Access Network Services
OS Platform Library
Application
WiFi
Cellular
Bluetooth
USB
PPP Context
PPP Context
The handoff to WiFi is completely controlled
by the cellular
access network operator, and a PPP context between the device and the operator is maintained

## Slide 39: Google in charge!
Internet
WiFi
Cellular
USB
Access Network Services
Virtual Connection Server
Virtual Connection Client
OS Platform Library
Application
Access Network Services
The Google Fi Approach:
OS-Controlled Seamless
Handoff Agility

## Slide 40: Mobility as a Simple Utility
Mobile Access Operators are being pushed into undistinguished utility roles
  No more voice premiums
  Erosive pressure on data service margins
  Pressure from WiFi service operators
  OS and App providers splitting away from carrier constraints
  Multi-Interface support turns mobile devices into opportunistic scavengers!

## Slide 41: Mobility Paranoia
Mobile Device manufacturers are being squeezed (except perhaps Apple!)
Google and Apple now control the platform space
Mutual trust issues are emerging between them
  Such as Apple’s Ad Blocker in iOS 9
Apps are now turning on their own versions of paranoia!
  In a market that is topping out in revenue terms each provider is attempting to protect itself by ring fencing its relationship with the end user

## Slide 42: What we want
Consumers want more for less
  The love/hate relationship with ads and ad-funded services
  The rise of the content streamers
  (much) higher download speeds
  (much) larger data caps
  Lower premiums
  Competitive pressure on providers to respond to this consumer pressure

## Slide 43: What we can’t get!
Exclusive Use radio spectrum is too expensive
  High access speeds require greater spectrum use per endpoint device
  Which can only be met with denser base station deployment (or lower access speeds)
  The increased spectrum demand and the lack of a price premium for high speed services implies lower revenue yield from the radio spectrum access license costs
  And there is no end in sight to this conundrum

## Slide 44: Where now?
Has exclusive use radio spectrum outpriced itself in today’s market?
  Consumers want WiFi performance for WiFi prices from the cellular radio network
  And that’s a problem when you have to pay large sums for an exclusive use spectrum license!

## Slide 45: Handing Off Mobiles
With no ability to drop data prices without taking a hit on their bottom line cellular access providers have limited means to respond
    Unless they can drop unit pricing and increase data caps then these cellular access providers pricing themselves out of the consumer market
    Competitive WiFi access and application handover approaches are placing pressure on the traditional mobile operator’s margins
If the cellular providers want cheaper carriage then they need to look at augmenting their offering with WiFi base station handoff infrastructure and perform automated handoff from the cellular network to a WiFi access network

## Slide 46: Who is Handing Off to Whom?
But the cellular operator has limited control over the handset’s behaviour!
And the handset has limited control over the OS behaviour!
And the OS has limited control over the application’s behaviour!

## Slide 47: Where now for Mobiles?
The underlying observation here is that the mobile network operator has lost control of the mobile access device and the services offered across the mobile network

## Slide 48: Where now for Mobiles?
And after losing that control there is no way back!
  The device OS platform vendors and the applications are charting a course that is in direct conflict with the mobile network operator’s desires
  They are managing to monetize this far more efficiently than the mobile network operator
  Apple and Google are winning (for the moment!)

## Slide 49: Where now for Mobiles?
  Mobile operators are trying to confront competitive pressures with their own WiFi handoff approaches, while OS platforms and Apps are trying to place themselves in control and constrain the mobile providers into limited cellular data role

## Slide 50: Where now for Mobiles?
  Which means that there is increasing pressure to increase the shared unregulated spectrum allocation and increasing discontent with the behaviour of the exclusive spectrum holders
  Pressure for more regulated exclusive access spectrum allocations from the incumbent operators
  Pressure for more unregulated open access (WiFi) spectrum allocations from users and alternate providers
  Public Policy pressure between direct license payments from incumbents and indirect economic efficiency outcomes from alternate use models

## Slide 51: Where now for Mobiles?
  Which means that there is increasing pressure to increase the shared unregulated spectrum allocation and increasing discontent with the behaviour of the exclusive spectrum holders
  Pressure for more regulated exclusive access spectrum allocations from the incumbent operators
  Pressure for more unregulated open access (WiFi) spectrum allocations from users and alternate providers
  Public Policy pressure between direct license payments from incumbents and indirect economic efficiency outcomes from alternate use models
Mobility is here to stay – that’s for sure!
But the tensions between exclusive use and shared access spectrum models will continue for some time
We are now exploring MIMO antenna technology and higher frequencies to push WiFI into Gbps
And the cellular folk are exploring 5G technologies which are also promising Gbps throughput

## Slide 52: Looking Forward (dimly)
Mobility is just too handy
Chips will get smaller
Power drain will get smaller
The single unit general purpose computer and packaged applications model is under pressure to change
Exactly how it will change is anyone’s guess
But it will change

## Slide 54: That’s it!