## Slide 1: Routing in 2016
Geoff Huston
Chief Scientist, APNIC

## Slide 2: Through the Routing Lens
There are very few ways to assemble a single view of the entire Internet
The lens of routing is one of the ways in which information relating to the entire reachable Internet is bought together
Even so, its not a perfect lens…

## Slide 3
1994: Introduction of CIDR
2001: The Great Internet Boom and Bust
2005: Broadband to the Masses
2009: The GFC hits the Internet
2011: Address Exhaustion
Routing the Internet
This is a view pulled together from each of the routing peers of Route-Views

## Slide 4: 2015-2016 in detail

## Slide 5: 2015-2016 in detail
average growth trend
Route Views Peers
RIS Peers

## Slide 6: Routing Indicators for IPv4
Routing prefixes – growing by some 54,000 prefixes per year

## Slide 7: Routing Indicators for IPv4
AS Numbers– growing by some 3,450 prefixes per year

## Slide 8: Routing Indicators for IPv4
More Specifics are still taking up one half of the routing table

## Slide 9: Routing Indicators for IPv4
But the average size of a routing advertisement is getting smaller

## Slide 10: Routing Indicators for IPv4
Address Exhaustion is now visible in the extent of advertised address space

## Slide 11: Routing Indicators for IPv4
The “shape” of inter-AS interconnection appears to be relatively steady, as the Average AS Path length has been steady through the year

## Slide 12: AS Adjacencies (Route-Views)
6,202 AS6939 HURRICANE - Hurricane Electric, Inc., US
5,069 AS174 COGENT-174 - Cogent Communications, US
4,767 AS3356 LEVEL3 - Level 3 Communications, Inc., US
2,632 AS3549 LVLT-3549 - Level 3 Communications, Inc., US
2,397 AS7018 ATT-INTERNET4 - AT&T Services, Inc., US
1,959 AS209 CENTURYLINK-US-LEGACY-QWEST - Qwest, US
1,953 AS57463 NETIX , BG
1,691 AS37100 SEACOM-AS, MU
1,620 AS34224 NETERRA-AS, BG
19,700 out of 57,064 ASNs have 1 or 2 AS Adjacencies (72%)
3,062 ASNs have 10 or more adjacencies
22 ASNs have >1,000 adjacencies

## Slide 13: What happened in 2016 in V4?
Routing Business as usual – despite IPv4 address exhaustion!
  From the look of the growth plots, its business as usual, despite the increasing pressures on IPv4 address availability
  The number of entries in the IPv4 default-free zone is now heading to 700,000 by the end of 2017
  The pace of growth of the routing table is still relatively constant at ~54,000 new entries and 3,400 new AS’s per year
    IPv4 address exhaustion is not changing this!
    Instead, we are advertising shorter prefixes into the routing system

## Slide 14: How can the IPv4 network continue to grow when we are running out of IPv4 addresses?
We are now recycling old addresses back into the routing system
Some of these addresses are transferred in ways that are recorded in the registry system, while others are being “leased” without any clear registration entry that describes the lessee

## Slide 15: IPv4 Advertised Address “Age”
80% of all new addresses announced in 2010 were allocated or assigned within the past 12 months
2% of all new addresses announced in 2010 were >= 20 years ‘old’ (legacy)
2010

## Slide 16: IPv4 Advertised Address “Age”
24 % of all new addresses announced in 2016 were allocated or assigned within the past 12 months
39 % of all new addresses announced in 2016 were >= 20 years ‘old’ (legacy)
2016

## Slide 17: IPv4: Advertised vs Unadvertised Addresses

## Slide 18: IPv4: Unadvertised Addresses

## Slide 19: IPv4:Assigned vs Recovered
Growth in Advertised Addresses
Change in the Unadvertised Address Pool
RIR Allocations
“recovery”
“draw down”

## Slide 20: IPv4 in 2016
The equivalent of 1.8 /8s was added to the routing table across 2016
Approximately 1.3 /8s were assigned by RIRs in 2015
  0.7 /8’s assigned by Afrinic
  0.2 /8s were assigned by APNIC, RIPE NCC (Last /8 allocations)
  0.1 /8s were assigned by ARIN, LACNIC
And a net of 0.5 /8’s were recovered from the Unadvertised Pool

## Slide 21: The Route-Views view of IPv6
World IPv6 Day
IANA IPv4 Exhaustion

## Slide 22: 2015-2016 in detail

## Slide 23: Routing Indicators for IPv6
Routing prefixes – growing by some 6,000 prefixes per year

## Slide 24: Routing Indicators for IPv6
AS Numbers– growing by some 1,700 prefixes per year (which is half the V4 growth)

## Slide 25: Routing Indicators for IPv6
More Specifics now take up more than one third of the routing table

## Slide 26: Routing Indicators for IPv6
The average size of a routing advertisement is getting smaller

## Slide 27: Routing Indicators for IPv6
Advertised Address span is growing at a linear rate

## Slide 28: Routing Indicators for IPv6
The “shape” of inter-AS interconnection in IPv6 appears to be steady, as the Average AS Path length has been held steady

## Slide 29: AS Adjacencies (Route Views)
9,105 out of 13,197 ASNs have 1 or 2 AS Adjacencies (69%)
917 ASNs have 10 or more adjacencies
4 ASNs have >1,000 adjacencies
3,276 AS6939 HURRICANE - Hurricane Electric, Inc., US
1,607 AS174 COGENT-174 - Cogent Communications, US
1,310 AS3356 LEVEL3 - Level 3 Communications, Inc., US
1,112 AS37100 SEACOM-AS, MU

## Slide 30: IPv6 in 2015
Overall IPv6 Internet growth in terms of BGP is steady at some 6,000 route entries p.a.
  This is growth of BGP route objects is 1/9 of the growth rate of the IPv4 network – as compared to the AS growth rate which is 1/2 of the IPv4 AS number growth rate

## Slide 31: What to expect

## Slide 32: BGP Size Projections
For the Internet this is a time of extreme uncertainty
    Registry IPv4 address run out
    Uncertainty over the impacts of market-mediated movements of IPv4 on the routing table
    Uncertainty over the timing of IPv6 takeup leads to a mixed response to IPv6 so far, and no clear indicator of trigger points for change for those remaining IPv4-only networks

## Slide 33: V4 - Daily Growth Rates

## Slide 34: V4 - Daily Growth Rates

## Slide 35: V4 - Relative Daily Growth Rates

## Slide 36: V4 - Relative Daily Growth Rates
Growth in the V4 network appears to be constant at a long term average of 120 additional routes per day, or some 45,000 additional routes per year
Given that the V4 address supply has run out this implies further reductions in address size in routes, which in turn implies ever greater reliance on NATs

## Slide 37: IPv4 BGP Table Size Predictions
Jan 2013 441,000
2014 488,000
2015 530,000
2016 586,000 580,000
2017 646,000 628,000 620,000
2018 700,000 675,000 670,000
2019 754,000 722,000 710,000
2020 808,000 768,000 760,000
2021 862,000 815,000
2022 916,000
Jan 2016 PREDICTION
Jan 2015 PREDICTION
Jan 2017 PREDICTION

## Slide 38: V6 - Daily Growth Rates

## Slide 39: V6 - Relative Growth Rates

## Slide 40: V6 - Relative Growth Rates
Growth in the V6 network appears to be increasing, but in relative terms this is slowing down.
Early adopters, who have tended to be the V4 transit providers, have already received IPv6 allocation and are routing them. The trailing edge of IPv6 adoption are generally composed of stub edge networks in IPv4. Many of these networks appear not to have made any visible moves in IPv6 as yet.
If we see a change in this picture the growth trend will likely be exponential. But its not clear when such a tipping point will occur

## Slide 41: IPv6 BGP Table Size predictions
Jan 2014 16,100
2015 21,200
2016 27,000
2017 35,000
2018 50,000 43,000
2019 65,000 51,000
2020 86,000 59,000
2021 113,000 67,000
2022 150,000 75,000
Exponential Model
Linear Model
Range of potential outcomes

## Slide 42: BGP Table Growth
Nothing in these figures suggests that there is cause for urgent alarm -- at present
  The overall eBGP growth rates for IPv4 are holding at a modest level, and the IPv6 table, although it is growing at a faster relative rate, is still small in size in absolute terms
  As long as we are prepared to live within the technical constraints of the current routing paradigm, the Internet’s use of BGP will continue to be viable for some time yet
  Nothing is melting in terms of the size of the routing table as yet

## Slide 43: BGP Updates
What about the level of updates in BGP?
Let’s look at the update load from a single eBGP feed in a DFZ context

## Slide 44: IPv4 Announcements and Withdrawals

## Slide 45: IPv4 Convergence Performance

## Slide 46: Updates in IPv4 BGP
The number of updates per instability event has been relatively constant
  Which is good, but why is this happening?
    Likely contributors to this outcome are the damping effect of widespread use of the MRAI interval by eBGP speakers, and the topology factors, as seen in the relatively constant V4 AS Path Length

## Slide 47: V6 Announcements and Withdrawals

## Slide 48: V6 Convergence Performance
High noise components in IPv6

## Slide 49: V6 Updated prefixes per day

## Slide 50: V6 Updates per event

## Slide 51: Updates in IPv6
BGP Route Updates are very unequally distributed across the prefix set – they appear to affect a very small number of prefixes which stand out well above the average

## Slide 52: Updates in IPv6
The busiest 50 IPv6 prefixes accounted for 1/2 of all BGP IPv6 prefix updates
http://bgpupdates.potaroo.net/instability/v6-bgpupd.html

## Slide 53: Compared to IPv4
IPv6
IPv4
http://bgpupdates.potaroo.net/instability/bgpupd.html
http://bgpupdates.potaroo.net/instability/v6-bgpupd.html

## Slide 54: Updates in IPv6 BGP
IPv6 routing behaviour is similar to IPv4 behaviour:
  Most announced prefixes are stable all of the time
  And as more prefixes are announced, most of these announced prefixes are highly stable.
  But for a small number of prefixes we observe highly unstable behaviours that dominate IPv6 BGP updates which appear to be more unstable (relatively) than IPv4

## Slide 55: Today’s State of Routing
“Mostly Harmless”
  The levels of growth of the tables, and the levels of growth of updates in BGP do not pose any immediate concerns
  The trends are predictable and steady, so network operators can plan well in advance for the capacity of routing equipment to meet their future needs
  But:
  The advanced levels of instability by a small number of networks are always annoying! How can we prevent these highly unstable prefixes?

## Slide 56: That’s it!
Questions?