## Slide 1: IPv6 Reliability Measurements
Geoff Huston
APNIC Labs

## Slide 2: The Question is…
Does IPv6 perform “better” than IPv4?

## Slide 3: The Question is…
Does IPv6 perform “better” than IPv4?
Is it more reliable?
Is it faster?

## Slide 4: The Measurement
The measured endpoint retrieves two URLs from the same remote server – one using IPv4 and the other using IPv6
  Unique DNS names and TLS are used to ensure that caching does not play a role in the measurement
We perform full packet capture at the server
We measure some 12M sample points each day and some 22% of these measurements use both IPv4 and IPv6

## Slide 5: Analysis
We look at the SYN/ACK exchange at the start of the TLS session
The time between receipt of the SYN and the subsequent ACK at the server is no less than one RTT between the server and the endpoint (and is a reasonable first order substitute for an RTT)
A received SYN with no subsequent ACK is interpreted as a failed connection attempt
Client
Server
1 RTT

## Slide 6: Analysis - Reliability
Why measure SYN handshake failure?
In a dual stack environment many of the most widely used apps (browsers) use Happy Eyeballs to decide which protocol to select
Happy Eyeballs bases its decision on the first protocol to complete a TCP SYN handshake
So TCP handshake failure will strongly influence this decision

## Slide 7: Analysis - Speed
Why measure only the handshake delay? Why not measure a larger data transfer?
Because in the end host and the server the same TCP version is used on top of IPv4 and IPv6
  If the end to end paths are the same in IPv4 and IPv6 we would see precisely the same session throughput
RTT and packet loss probability determine session throughput
  In this experiment we use the RTT as in indicator of path difference

## Slide 8: IPv6 TCP Connection Failure

## Slide 9: IPv6 TCP Connection Failure
The global failure rate of some 1.4% is better than earlier data (4% failure in early 2017), but its still bad
We cannot detect failure in attempting to deliver a packet from the client to the server – what we see as “failure” is a failure to deliver an IPv6 packet from the server to the client
Possible reasons:
  Endpoint using an unreachable IPv6 address
  End site firewalls and filters
  Transition mechanism failure

## Slide 10: The Good
This 464XLAT mobile network
(T-Mobile) has remarkably small failure rates – the endpoints are connected via native IPv6 and as this is a mobile network there is only a small amount of customer-operated filtering middleware

## Slide 11: 464XLAT Performance
These networks operate in a “native” IPv6 mode
IPv6 connections to a server require no network processing and no client handling

## Slide 12: The Good
Similar story in India with Reliance JIO – the endpoints are connected via native IPv6 and as this is a mobile network there is only a small amount of customer-operated filtering middleware

## Slide 13: The Bad
Seriously?
A 6%-10% IPv6 connection failure rate is bad enough
A sustained high failure rate for over 2 years seems worse!

## Slide 14: The Appalling!

## Slide 15: High IPv6 Failure Levels

## Slide 16: High IPv6 Failure Levels

## Slide 17: High IPv6 Failure Levels

## Slide 18: High IPv6 Failure Levels

## Slide 19: High IPv6 Failure Levels

## Slide 20: Thailand

## Slide 21: The big picture

## Slide 22: Comment
For many end users in Vietnam, New Zealand, Guatamala, Colombia and China their IPv6 service looks pretty broken
  The combination of Dual Stack and Happy Eyeballs masks the problem so that the user does not experience a degraded service
  But this only will work while Dual Stack is around
Other ISPs have managed to do a much better job, such as in the United States, Sweden, Thailand and Korea and the IPv6 connection failure rates are close to experimental noise levels
What’s happening in the second set of countries and ISPs that is NOT happening in the first set?

## Slide 23: Transition Technologies
Stateful transition technologies that involve protocol translation show higher levels of instability
Translation technologies that require orchestration of DNS and network state are also more unstable

## Slide 24: Dual Stack is NOT the Goal
Despite all the grim predictions that IPv4 will be around for a long time to come, the aim of this transition is NOT to make Dual Stack work optimally
The goal is to automatically transition the network to operate over IPv6
The way to achieve this is for client systems to prefer to use IPv6 whenever it can

## Slide 25: Happy Eyeballs
An unconditional preference for IPv6 can lead to some very poor user experience instances
  Linux uses a 108 second connection timer, for example
Applications (particularly browsers) have used a “Happy Eyeballs” approach
DNS Resolution
TCP Handshake
50ms AAAA Delay
250ms IPv6 Delay
DNS A and AAAA are fired off at the same time – if the A response comes back first then the application will start a 50ms timer to wait for a AAAA response
A TCP session will be started in IPv6 if there is a IPv6 address record. If the handshake is not completed within 250 ms then an IPv4 TCP session is also fired off

## Slide 26: Tuning IPv6 for Happy Eyeballs
When connecting to a remote dual stack service, the Routing Path selection for IPv6 should be similar to IPv4
Where there are path deviations, the path discrepancy should be contained
This is not always the case…

## Slide 27: India, late 2016

## Slide 28: Vodaphone New Zealand - 2019

## Slide 29: Vodaphone New Zealand - 2019

## Slide 30: Sometimes it’s the DNS!
Happy Eyeballs assumes that the time to resolve an A and a AAAA record are within 50 msecs of each other
The client generates a query for the A record and a second query for a AAAA record at the same time
The recursive resolver does not necessarily process the two requests in parallel:
  A QNAME minimisation resolver may use A queries to walk the DNS hierarchy
  A DNS-based content filter may use A queries to determine the outcome
  In a partial deployed state its more likely that the A record is already in the local cache

## Slide 31: Worldwide RTT Diff Performance
The overall trend was improving through 2018. The picture appears to have reversed in 2019

## Slide 32: China’s IPv6 Network

## Slide 33: 3 Suggestions to Assist IPv6 Robustness
Avoid stateful IPv6 -> IPv4 transition mechanisms if possible – if you can operate IPv6 in native mode all the better!
Avoid using IPv6-in-IPv4 encapsulations
  Not only are tunnels unstable, but the reduced IPv6 MTU may cause problems with extension header based packet discard
Keep IPv4 and IPv6 paths congruent if possible
  Yes, this can be really challenging for multi-homed networks, but try to use transit and peer arrangements that are dual stack

## Slide 34: But that’s not all…
IPv6 used a new approach to extension headers, including packet fragmentation by inserting them between the IPv6 header and the transport header
Which means that hardware will have to spend cycles to hunt for a transport header
Or it can just drop the packet…
IPv6 header
Payload
TCP/UDP xtn header
Fragmentation xtn header

## Slide 35: 2017 Measurement
This measurement test involved sending a fragmented UDP packet to recursive resolvers

## Slide 36: 2017 Measurement
This measurement test involved sending a fragmented TCP packet to browser endpoints

## Slide 37: What can we say?
There are ongoing issues with IPv6 reliability in many parts of the world
  This appears to relate to local security policies at the client edge of the network
  We can expect most of this to improve over time by itself

## Slide 38: What can we say?
But there are also very serious issues with Path MTU management and handling of IPv6 extension headers
  This is a more challenging issue that will probably not just clean itself up over time
  Should we just avoid IPv6 extension headers?
  Or try to clean up the IPv6 switching infrastructure?

## Slide 39: What can we say?
But there are also very serious issues with Path MTU management and handling of IPv6 extension headers
  This is a more challenging issue that will probably not just clean itself up over time
  Should we just avoid IPv6 extension headers?
  Or try to clean up the IPv6 switching infrastructure?
Unlikely!

## Slide 40
Thanks!